## Slide 1
The S-Cycle Model
Laura Hay
Alex Duffy
Department of Design, Manufacture and Engineering Management
University of Strathclyde
e: laura.hay@strath.ac.uk
t: +44(0)141 574 5293
Knowledge, Understanding and
Competence in SE and Sustainability
Copyright © 2015 by Laura Hay

## Slide 2
Overview
Definitions and applications of sustainability.
Introduction to the S-Cycle model.
Case studies undertaken to test/demonstrate the model.
Questions.

## Slide 3
What is sustainability?
sustainable development
sustainable consumption & production
sustainable business/ corporate sustainability
sustainable product development
Sustainable technical systems?

## Slide 4
the ability to be maintained by something
What is sustainability?
the ability to sustain
the ability to continue
the ability to maintain something
literal interpretation
closely related
behaviour for sustainability
behaviour meets sustainability performance criteria
the ability to maintain something, with respect to these criteria
our research

## Slide 5
Research in DMEM at the University of Strathclyde
sustainability in engineering design
focus area
different domains
different targets to be maintained
sustainable engineering
sustainability of consumerism
sustainable design
design activity & design output
system function/ system output
product value
Applications of sustainability

## Slide 6
The S-Cycle model - overview
systems exhibit behaviour for sustainability
the S-Cycle describes the material and energetic aspects of behaviour that affect technical system sustainability (i.e. that we should measure)
generic  applicable to different technical systems
general concepts of activity and system form the foundation of the model…

## Slide 7
...technical systems produce waste (W) as well as their intended output
mechanisms
compress refrigerant
activity
e.g. flow of refrigerant to a condenser (O)
e.g. electricity, refrigerant, oil
Activity
goals
output
inputs
...use inputs to produce an intended output (O) that satisfies the goal of the activity
e.g. compressor & oil system, human operators
e.g. pressure & flow rate of refrigerant
e.g. heat energy (W)
W
Provides a way to represent the behaviour of a technical system, e.g. a compressor…
mechanisms

## Slide 8
e.g. direct inputs + indirect inputs of fossil-derived energy for extraction, manufacturing & recycling
e.g. direct inputs + indirect inputs of biomass-derived energy for extraction, manufacturing & recycling
non-renewable resources (NR)
e.g. components produced using renewable energy
e.g. components produced using fossil fuels
renewable resources (R)
e.g. human operators
e.g. obosolete components
Across the life cycle:
Activity
...resources may be renewable (R) or non-renewable (NR)
renewable resources (R)
non-renewable resources (NR)
e.g. direct inputs of fossil-derived energy
e.g. direct inputs of biomass-derived energy
system goals
(R)
(R)
(NR)
(NR)
e.g. flow of refrigerant to a condenser (O)
e.g. heat energy (W)
compress refrigerant
mechanisms
goals
output
inputs
Operation phase:
e.g. waste materials & energy from extraction, manufacturing & recycling

## Slide 9
system goals + sustainability goals
...should not be produced faster than it can be processed
...should not be used faster than stocks can regenerate
Activity
...additional goals for system sustainability
system goals
(R)
(R)
(NR)
(NR)
...should not be used
e.g. flow of refrigerant to a condenser (O)
e.g. heat energy (W)
compress refrigerant
mechanisms
goals
output
inputs
...the technical system may also produce its own resources (intended resources, IR)
e.g. oil re-injected to compressor (IR)
IR
e.g. obosolete components
e.g. human operators
e.g. direct inputs of biomass-derived energy
e.g. direct inputs of fossil-derived energy

## Slide 10
natural NRR stocks e.g. crude oil, coal & natural gas deposits
e.g. the stock of equipment on board the ship
e.g. stocks of oil & refrigerant on board, the sea & atmosphere
natural RR stocks e.g. forests, oceans, the atmosphere
All technical systems operate within a wider system of interest…
activity
NRR
system goals + sustainability goals
System
non-renewable resource stocks
IR
W
O
RR
RR
NRR
system of interest
renewable resource stocks
…that provides resources…
compress refrigerant
the global ecosystem
a ship at sea
…and receives intended output and waste.
mechanisms
goals
output
inputs
For example…

## Slide 11
System
activity
non-renewable resource stocks
renewable resource stocks
system of interest
Resources and waste flow throughout the system of interest…
system goals + sustainability goals
RR
RR
NRR
NRR
RR
O
O
IR
IR
mechanisms
goals
output
inputs

## Slide 12
activity
system goals + sustainability goals
RR
RR
NRR
NRR
RR
O
O
S-Cycle model
non-renewable resource stocks
renewable resource stocks
system of interest
IR
IR
mechanisms
goals
output
inputs

## Slide 13
…what resources are produced for self-support (intended resources, IR)?
…and what waste (W) must be mitigated?
…within the boundary of a particular system of interest…
…from a sustainability perspective.
To sustain the production of intended output (O) over time…
…what renewable (RR) and non-renewable (NRR) resources are required?
The S-Cycle supports the modelling & assessment of a technical system’s behaviour…
The S-Cycle model - recap

## Slide 14
modelling
action
S-Cycle Performance Improvement Process
performance assessment & analysis
review

## Slide 15
S-Cycle case studies
S-Cycle model applied to model and interpret the behaviour of the chilled water (CW) system on a ship (case study 1).
Model of system behaviour used as a basis to (case study 2):
identify sustainability goals and metrics for the CW plant sub-system
develop a quantitative model to estimate CW plant performance
CW plant sustainability performance evaluated, and potential areas for improvement identified.
Steps 1 – 4 of the S-Cycle Performance Improvement Process (modelling & assessment/analysis.
Focused on a portion of the operation phase of the life cycle – ship operational at sea.

## Slide 16
activity
Remove waste heat from equipment aboard the ship
goals
outputs
inputs
mechanisms
CW system activity:
IDEF0 language applied to decompose activity/sub-activity relationships.
materials & energy
CW system equip., human operators
Modelling behaviour – IDEF0

## Slide 17
Inputs
Mechanisms
Controls (conditions that govern the outputs)
Outputs
Activity
Sub-activities
Coupling relationships

## Slide 18
Interpreting behaviour

## Slide 19
Resource stocks = the sea & atmosphere (natural), and stocks on board the ship (man-made)…
The S-Cycle was applied to each activity in the CW system model…
ship at sea
…i.e. the stocks available whilst the ship is at sea.
…to classify the inputs, outputs & mechanisms as renewable, non-renewable & intended resources, intended outputs, or waste.
Interpreting behaviour
Remove waste heat

## Slide 20
Interpreting behaviour
IDEF0 Diagram | Activity | Renewable resources | Non-renewable resources | Intended resources | Intended outputs | Waste
A0 | Absorb waste heat from users | CW flow & supply temp. (Ia) | CW users/CWS heat exchange mechs. (Mb) | ----------------------- | CW flow & return temp. (Oc) | -----------------------
A0 | Control & configure CWS | Electricity to CWS control sys. (I) | Human control interface (I) | ----------------------- | Informational  excluded | -----------------------
 |  | Humans (M) | Local control mechs. (I) |  |  | 
 |  |  | CWS control sys. (M) |  |  | 
 |  |  | Controllable CWP equip. (M) |  |  | 
 |  |  | Controllable CW circ. sys. equip. (M) |  |  | 
A0 | Accumulate & store cooling medium | Air (I) | H-tank equip. (M) | ----------------------- | Flow of water between H-tanks & CW circ. sys. | -----------------------
 |  | Water for storage in H-tanks (I) |  |  |  | 
A0 | Circulate cooling medium in CWS | CW flow & return temp. (I) | CW circ. sys. equip. (M) | ----------------------- | CW flow & return temp. (O) | Air from vacuum degassers (O)
 |  | Electricity to CW circ. sys. equip. (I) |  |  |  | Water losses from CW circ. sys. (O)
 |  |  |  |  |  | Energy losses in CW circ. sys. (O)
A0 | Chill cooling medium | CW flow & return temp. (I) | CWP equip. (M) | ----------------------- | CW flow & supply temp. (O) | Refrig. losses from CWP equip. (O)
 |  | Electricity to CWP equip. (I) |  |  |  | Energy losses in CWP equip. (O)
 |  | Oil in compressors (I) |  |  |  | SW flow & reject temp. (O)
 |  | SW flow & supply temp. (I) |  |  |  | 
 |  | Refrig. in CWPs (I) |  |  |  | 
A511 | Compress flow of refrigerant from evaporator | Flow of refrig. in suction line (I) | Compressor & oil circuit (M) | Oil re-injected to compressor | Flow of refrig. from compressor (O) | Energy losses in compressor (O)
 |  | Electricity to compressor (I) |  |  |  | 
 |  | Oil in CWP 1 compressor (I) |  |  |  | 
Excerpt from interpretation…
operation phase  direct inputs and outputs only
majority of material and energetic inputs interpreted as renewable since replenishable at sea
majority of physical equipment comprising the system interpreted as non-renewable since not fully replenishable at sea (partially owing to spares)
a single example of intended resources identified, i.e. oil re-injected to compressor crankcase inside CW plants
waste – mainly due to material leaks (e.g. refrigerant and water), and energy losses (e.g. heat and vibration)
identified an additional type of input not included in the first version of the model – contaminants, inputs detrimental to sustained production of intended output

## Slide 21
Identifying sustainability goals & metrics
Masters project focusing on performance of CW plant sub-system during design process…
Minimise of use resources that are harmful to the environment
Minimise cost of intended output (sustainable business/sustainable development goal)
Minimise production of waste
Maximise intended resources?

## Slide 22
Assessing sustainability performance
Metrics and measures defined to assess system performance against each goal…
Test data, data from quantitative model, and benchmarking used to evaluate metrics & measures…
…metric values analysed to identify areas for improvement (primarily reduction in diesel consumption associated with electrical input).